## Slide 1
CONFINED SPACE
OPERATIONS
TRAINING
Entrant • Attendant • 4-Gas Monitoring • H₂S Safety
Mixed audience: operators, maintenance teams, contractors, attendants, and supervisors
1
PLAN
2
MONITOR
3
PROTECT
4
RESPOND
Notes: Introduce the course and emphasize stop-work authority.

## Slide 2
1. WHAT IS A CONFINED SPACE?
2
A confined space is a space that:
Is large enough for an employee to bodily enter and perform work.
Has limited or restricted means for entry or exit.
Is not designed for continuous employee occupancy.
TWO TYPES
Permit-Required Confined Space: hazards require a permit.
Non-Permit Confined Space: no hazard capable of serious harm.
Examples in oil & gas: tanks, vessels, pits, manholes, pipelines, ducts, vaults, and heat exchangers.

## Slide 3
2. ROLES & RESPONSIBILITIES
3
E
ENTRANT
Enters the space, follows procedures, wears PPE, communicates, and exits when ordered or when an alarm activates.
A
ATTENDANT
Remains outside, tracks entrants, monitors conditions, controls access, and summons rescue if needed.
S
ENTRY SUPERVISOR
Verifies controls and testing, authorizes entry, and cancels the permit when conditions change.

## Slide 4
3. CONFINED SPACE HAZARDS
4
!
ATMOSPHERIC HAZARDS
Oxygen deficiency or enrichment
Flammable atmosphere
Toxic gases such as H₂S or CO
▲
PHYSICAL HAZARDS
Engulfment and poor visibility
Heat stress and slippery surfaces
Poor lighting and excessive noise
⚙
MECHANICAL / ELECTRICAL
Moving equipment
Electrical shock
Pressurized lines and energy sources
IF CONDITIONS CHANGE: STOP WORK • EXIT • RE-EVALUATE

## Slide 5
4. 4-GAS METER
5
A 4-gas meter detects four potentially dangerous atmospheric conditions:
O₂
Oxygen
19.5%–23.5% safe range
LEL
Combustible gas
Below 10% LEL
CO
Carbon monoxide
Follow site action levels
H₂S
Hydrogen sulfide
Follow site action levels
BUMP TEST
Before each use
CALIBRATE
Per manufacturer and company policy

## Slide 6
5. CONTINUOUS ATMOSPHERIC MONITORING
6
1
BEFORE ENTRY
Test from the top, middle, and bottom of the space.
2
DURING ENTRY
Continuously monitor while entrants are inside.
3
ALARM RESPONSE
If any alarm sounds, evacuate immediately and investigate.
4
SAFE LIMITS
O₂: 19.5%–23.5% LEL: <10% CO/H₂S: site action levels
ONE TEST IS NEVER ENOUGH — CONDITIONS CAN CHANGE QUICKLY

## Slide 7
6. HYDROGEN SULFIDE (H₂S) SAFETY
7
H₂S
PROPERTIES
Colorless, toxic, heavier than air, and flammable. Odor is not reliable.
2
EXPOSURE SYMPTOMS
Low exposure: irritation, headache, nausea. High exposure: collapse or respiratory failure.
3
PROTECT YOURSELF
Rely on monitors, follow respiratory-protection rules, evacuate immediately if alarms activate.
NEVER RELY ON SMELL — USE MONITORING AND THE SITE EMERGENCY PLAN

## Slide 8
7. EMERGENCY RESPONSE
8
1
STOP WORK
Stop immediately if conditions become unsafe.
2
EXIT IMMEDIATELY
Evacuate and warn others.
3
NON-ENTRY RESCUE
Do not enter unless trained and equipped.
4
COMMUNICATE
Notify the supervisor and emergency response.

## Slide 9
8. DECISION POINT: SHOULD YOU ENTER?
9
SCENARIO
The entry permit is complete, but the 4-gas monitor has not been bump tested today.
What should the crew do?
A
Enter because the permit is signed.
B
Enter and test the meter after entry.
C
Delay entry until the monitor is verified operational.
D
Borrow any available monitor without checking it.
Learning point: Stop Work Authority applies before entry begins.

## Slide 10
9. DECISION POINT: ATMOSPHERE CHANGES
10
SCENARIO
During entry, oxygen drops from 20.9% to 18.8% and the meter alarms.
1
Exit the confined space immediately.
2
Notify the attendant and supervisor.
3
Do not re-enter until the hazard is eliminated and testing confirms acceptable conditions.
Never troubleshoot the hazard from inside the space.

## Slide 11
10. PERFORMANCE SUPPORT: ENTRY CHECKLIST
11
BEFORE ENTRY
Permit approved
Hazards identified
LOTO/isolation verified
Rescue plan reviewed
4-gas monitor bump tested
PPE/retrieval equipment inspected
DURING ENTRY
Continuous monitoring
Attendant present
Communication maintained
Permit conditions followed
No unauthorized entrants
IF CONDITIONS CHANGE
Stop Work
Exit immediately
Notify supervisor
Activate emergency response
Secure area

## Slide 12
11. KNOWLEDGE CHECK
12
?
Choose the best answer. Discuss as a group before revealing the answer key.
1. Which gas can cause rapid loss of consciousness and death at high ppm?
A. Oxygen B. LEL C. CO D. H₂S
2. Who remains outside the space and monitors entrants?
A. Entrant B. Attendant C. Supervisor D. Observer
3. What is the safe oxygen range for entry?
A. 18–21% B. 19.5–23.5% C. 21–25% D. 18–24%
4. If the gas meter alarms during entry, what should be done first?
A. Investigate B. Continue C. Exit immediately D. Increase ventilation
5. What document authorizes permit-required confined space entry?
A. Work Order B. JSA C. Entry Permit D. Safety Checklist
Answer key: 1-D, 2-B, 3-B, 4-C, 5-C

## Slide 13
12. FINAL ASSESSMENT
13
Match each responsibility to the correct role.
Responsibility
Entrant
Attendant
Supervisor
Wears PPE
✓
Maintains entrant count
✓
Authorizes entry permit
✓
Exits when alarm activates
✓
Prevents unauthorized entry
✓
Cancels permit
✓
True / False: H₂S can deaden your sense of smell. | Continuous monitoring should continue throughout entry. | Workers have Stop Work Authority.

## Slide 14
13. FACILITATOR GUIDE
14
Audience
Operators, maintenance teams, contractors, attendants, and supervisors.
Duration
20–25 minutes with discussion and scenario questions.
Materials
Entry permit, 4-gas monitor, PPE/harness, rescue plan, site procedure.
Method
Instructor-led toolbox style, discussion-based, with a performance-support checklist.
Evaluation
Knowledge check, final assessment, and supervisor observation on the job.

## Slide 15
14. KEY TAKEAWAYS & SAFETY COMMITMENT
15
✓
Plan the work and control hazards.
✓
Verify and monitor the atmosphere.
✓
Know your role and follow procedures.
✓
Use equipment properly and communicate.
✓
H₂S can kill — monitor and stay alert.
✓
Stop work if conditions are unsafe.
SAFETY IS EVERYONE’S RESPONSIBILITY.
WORK SAFE. GO HOME SAFE.

## Slide 16
15. SOURCE & DESIGN NOTES
16
Primary regulatory reference
OSHA 29 CFR 1910.146 — Permit-Required Confined Spaces.
Atmospheric testing sequence: oxygen, combustible gases/vapors, then toxic gases/vapors.
Oxygen-deficient atmosphere: below 19.5%. Oxygen-enriched atmosphere: above 23.5%.
Company/site procedures determine alarm set points, H₂S response levels, respiratory protection, and rescue procedures.
Portfolio positioning: This deck demonstrates instructor-led training design, scenario-based decision points, role-specific responsibilities, field-checklist performance support, and assessment alignment for high-risk industrial operations.
Confined Space Operations Training | Portfolio Sample